DS homework 4	Hash tables	Eric Lief

Experimental design and procedure

Non-sequential (random) and sequential tests were carried out as specified in the description. I have fixed the errors pointed out to me in my initial implementation and regenerated the charts below.

Implementation

I implemented all structures in Java using Object-Oriented principles of design. There are two abstract base classes: Hash and HashTable.

Abstract Base classes

Hash
Hash encapsulates the data and behavior of the hash family one desires to implement. It has two basic methods (hash and rehash) which are implemented distinctly in the child classes. Its data fields include w (the size in bits of range of the function) and u (size in decimal).

Implemented as:

ModularHash	h(x) = x mod m
MultishiftHash	h(x) = ((a * x) mod |U|) / (|U| / m)
TabularHash	h(x) = T 1 (x 1 ) XOR T 2 (x 2 ) XOR ... XOR T c (x c )

HashTable
HashTable houses the basic information and methods of any hash table/map implementation, with its two methods insert and find. Its data includes the size of table (m) and number of elements (n).

Implemented as:

LinearProbeHT
CuckooHT

Notes

I implemented my own simple random generator since I had trouble using the suggested C tool in Java.

RandGenerator will output a random number (int, long or double) within a given range. I used this to simulate an unsigned int (like in C), in the range [0, 2^32-1]. As this exceeds the range for java int, I used long.

LinearProbeHT stores keys in a one-dimensional array. Since Java has no null for primitives, I chose -1 (since all generated numbers are positive). The class allows one to pass in a hash function, which can be rehashed if necessary (though this was only done for Cuckoo hashing),

CuckooHT , similar to LP, stores not one but two sets of keys in one-dimensional arrays, in addition to two hash functions. The insert method is implemented similarly to that described in Pagh and Rodler (2004) with several differences. I used a main loop in the insert method (do-while), controlled by maxSteps, in order to count steps and rehash (with or without resizing of the table as described in the article). I count steps locally and augment or decrement this count when the insertion or reinsertion is completed. The global (class variable) steps is also augmented to the local value after the insertion procedure.

maxSteps = log2 (n)

As we were supposed to keep m constant, I did not use resizing for this task. When the maximum allowed steps were exceeded, I merely rehashed the two hash functions (hashFuncA and hashFuncb), rebuild the table with these new hash functions, adding this local step count to the accumulated steps. I also limited the total rehashes in the experiment to no more than 10 failed attempts.

Task 1: Non-sequential (random) tests

Below I present the obtained results for each hash function and hash table combination in one plot individual plots are in the appendix.

Comparison of LP and Cuckoo Hashing
steps
load (a)
steps

Comparison of LP and Cuckoo Hashing
steps
load (a)
log(steps)

In regard to steps, it is evident that both hash tables behave quite differently. Linear Probing (LP) tables, regardless of the hash function used, perform quite similarly, and lp-mod and lp-mult are hidden under the blue lp-tab curve. It appears that steps experience exponential growth with increasing load factor for all tables. The second plot uses a logarithmic y-axis (steps) to see whether we are dealing with exponential growth of steps in LP as well as Cuckoo tables. LP does quite well at lower loads (a), arching upwards and starting to degrade (exponentially) at about .80 load. We can safely conclude from the results here that LP tables perform quite similarly and are quite insensitive to the choose of hash function (family).

Cuckoo hashing, however, show less of a steep ascent, even when approaching full load. There are, however, some differences with regard to the hash function used. For multiply-shift, we see a slightly better performance at lower loads and less of a spike upward as in tabulation at higher loads. However, the log plot shows a dive downward at around .9, which is indicative of complete failure. I experimented with different MAX_STEPS and MAX_FAILURES and found that performance was quite similar with the values below as for others such as 10/100.

MAX_REHASHES = log(m) = 20
MAX_STEPS = 2 * MAX_REHASHES = 2 * log(m) = 40

Cuckoo with tabulation exponentially decays almost merging with lp-tab.

Perhaps this difference is due to Cuckoo hash tables offering constant lookup time regardless of hash function, yet normally offer constant time for insertion with truly random hash functions. Tabulation, however, is reputedly known to experience failure as collisions become more and more frequent. In this task, high load factor was reached because of the somewhat tolerant parameters above, but once can get earlier failure by lowering these values.

It is therefore clear from the plot or averages (see below) that Cuckoo hashing is more sensitive to hash function than LP.

Let us now look at mean time per insert versus load.

Comparison of LP and Cuckoo
time vs. load
load
time (ns)

Comparison of LP and Cuckoo
time vs. load
load
log(time) (ns)

It is also apparent from the plots above that Cuckoo hashing performs worse than LP (here tabulation functions take longer). This is understandable when one takes into account the overhead for building and rebuilding the table (rehashes). Even with the optimization of this process by using bit masking (recall that I was using strings and splitting these and then converting to longs before, which was extremely inefficient), hashing is slower than its counterparts for both tables. Thus among all variants, tabulation performs the worse. In the second plot above, a logarithmic time scale is used, which aids in the detection of increasing rehashes for Cuckoo hashing at around .5 for tabulation and .65 for mult-shift.

The results are summarized in the table below, where we can see these trends of LP being quite stable and consistent, while cuckoo hashing show a lower mean steps but a greater growth in mean time per insert which is most extreme at higher loads (e.g. above .5).

Table 1: Averages across all loads for all combinations

Task 2: Sequential tests

In these tests, ordered integers were inserted into LP hash tables of varying sizes and the measurements read from .89 to .91 load. Thus the load is high to begin with, and we are examining the performance of LP with different hashing schemes. The length of the sequence inserted in each run was 4096 (212). I chose this value because Pagh and Rodler (2004) used it.

For the plots, the size along the x-axis is logarithmic—that is, it is l, such that m = 2l on the x-axis and the statistical values on the y-axis. 1000 runs were carried out for each size. The min, max, average, median and 90th percentile of are displayed below. Note that the minimum size used for these tests is l = 0 -> m = log 20 = 1.

The plots below reflect the dependence of mean steps on table size.

Sequential test for LP Mult-shift
log2(m)
mean steps

Sequential test for LP Mult-shift
log2(m)
log(steps)

Sequential for LP tabular
log2(m)
mean steps

Sequential for LP tabular
log2(m)
log(steps)

The two log-log plots above illustrate better the distribution of min, max, mean, median, and 90th percentile within each plot. A cross-comparison of both hash functions reveals two interesting differences First, mult-shift hashing (mean at 7.01 for all table sizes) performs better than tabulation (mean of 21.72). Second, tabular hashing is constant across all table sizes, whereas multi-shift degrades for higher loads (i.e. higher steps).

From the above two plots, maximum values occur for at 214 (4958.72) and 217 (3315.00 steps) for for mult-shift and tabulation respectively. Although mult-shift seems to perform better at higher loads (lower mean steps), its maximum value occurs in smaller table sizes is most marked than for tabulation. As we are inserting sequential items into a small table, there is a higher chance of collisions when using tabulation, but it overall takes less time to find a place in the table when using tabulation than when using mult-shift. This is understandable when we consider that tabulation (4-independent) approaches a truly random hash function in LP and Cuckoo tables (Petrascu and Thorup, 2010). Thus when filling the table up to high load, although the keys are more uniformly distributed due to the more random tabulation hash function, there is a greater chance of degradation. Thus if a collision occurs with LP, there is a greater chance that the tabulation scheme breaks down at higher loads as mentioned above than when using the mult-shift (2-independent) family.

Final notes (though speculative)

The L1 cache size of my computer is 32 KB (215). Recall that the length of the sequence inserted in each trial was 4096 (212). At this point a new run is begun, and this must be the peak we see in the above plots. As for the other peaks, we also see them in the tabulation scheme for average, median, and 90th percentile. Pagh and Rodler (2004) mention that LP is less sensitive to the choice of hash function than other schemes. However, we are seeing a sensitivity here related to cache size (for me 215 ). Thus at sizes above cache capacity we should expect a rise in time. In fact, a formula is given by the above authors:

Time = O + N · R · (1 − C/T ),

where 1 – C/T is the probability of a cache miss (greatest when the ratio of cache to dictionary size is smallest as T increases; smallest when both cache and table(s) are of equal size. The authors point out that the table must be larger than cache for the formula to hold. In our case, this wasn’t always so, but above 32 KB (215), the chance of a cache miss would be larger. In our experiment, we are not dealing with time, but rather steps, but it is possible that there is a correlation between cache misses.